## Slide 1
NLX
Natus
Extraction to mat file (40\2kHz)
Extraction to mat file (30\2kHz)
Transform to uV
Remove line noise (60Hz)
Transform to uV
Remove line noise (60Hz)
Create average reference (based on 8 electrodes in bundle), and remove from raw signal to get rid of large artifacts
getSpikes, doClustering
(wave_clus)
uChannels
downSample – 1kHz
uChannels (LFP)
MacroChannels
Detect (discard) interictal spikes, also remove noisy\bad channels, threshold for excluding channels with high rates of interictal spikes
ripple detection –
Detection based on power-spectrum
Validation – looking at the power spectrum and duration of average ripple on every channel included in the analysis
Using original referencing
EEG channels (Pz,Ez, C3, C4)
Synchronize spiking activity to behavior
Anatomical tracing of contacts and u-wires (Done by Rocelle) – choose MTL channels
Determining channel polarity – will determine if ripple peak is neg/pos (not critical for wake datasets)
Determining behavioral relevant timepoints based on maze log (start/N/D/G)
Color code -
Electrophysiology system
Clinical
Behavioral
Synchronization of neural data and behavioral log (laptop-based)
Localization of contacts in the brain (based on CT, MRI, implant plan) - iElvis
Bird’s eye view on pre-processing pipeline
Macros
Notes: C:\Maya\Dropbox\Code\Nir Lab\Work\preProcess\preProcessDepthUCLA(subj, exp)
Add synchronization between blackRock and NLX – based on stimulation
Add sleep scoring pipeline and synch to timestamps
Several bands of filters ([80-200], [300-500])
Add selection point – discard of channels at SOZ
Add selection-point – detect candidate channels for spindle analysis
Look at alternative options – (1) Neuron 2017, (2) Harris – KiloSort - neuroPixel software – analyzes stability over a prolonged period
Anatomical localizations

## Slide 2: RAW DATA COLLECTED PER SUBJECT
Behavior - Log file (timestamps based on laptop cup, quiz results, movement tracking) - daXXX_maze_log.csv
Neural recording - EDF files (can be opened via EDFBrowser)
  Comments tracking start/end of task
  DC channel for photodiode
  Basic tracking of noise
Pt Information in the room – time, pt number, age, handness, when was the last seizure (minimum 3-4h post seizure)
Anatomy – either through the BOX EEG folder, nurse, other researchers

## Slide 3: Analysis steps
Creating a montage file (spreadsheet is manual – daXXX.csv under ptData, examples of generated montage files are under MACRO_MONTAGE)
Synchronization – input files are the DC (photodiode output) + behavioral log
Documented here - iEEG-Maze-NeuralDrift\ANALYSIS\Synchronization\MazeiEEG-Maze-NeuralDrift\ANALYSIS\Synchronization\Maze
Manual process where you validate that the TTL-detections are accurate.
Pt-specific script – for example - IR106_extract_photoDiode_TTLs_template_Dec52024
Extract the EDF  .mat files
Extraction Per subject is done via scripts - preProcess_DAXXX which document the source, and the process of creating the processed LFP signal folder Maze_2.0\data_p\DAXXX\EXPX\Denoised_Downsampled_InMicroVolt\MACRO
It uses scripts like – getmemMazeExperimentHeader, preProcessDepthUCD, readEdfChannelLocal
Extracts the EDF
Cleans line noise
Resamples to 1kHz
Renames the channels based on the macromontage
Label bad channels in macro-montage - Box\iEEG_MAZE_project\CODE\iEEG_extraction (recommendations at badChans documentation.docx)
Identify areas of interest that are relevant to your analysis
Once the Macro channels are organized in the data_p folder, you can use –\memMaze-code\useExample_AnalyzeMazeNeuralActivity_MACRO.m
Class of functions that calculate neural markers, spectral analysis and stats